22.058, Principles of Medical Imaging

Fall 2002

Homework #4

Due Tuesday October 22nd

________________________________________________________________________

1. Write a complete system description for the instrument function of a planar x-ray imager (assume scanned fan beam).  Include:

• finite size source

• heal effect on source intensity and energy spectrum

• oblique angle effects

• depth dependent magnification

• quantum efficiency and PSF for the scintillator/photographic plate.

2. For a cylindrical object (long axis perpendicular to the beam) calculate the profile of X-ray intensity in a fan beam geometry, assuming that the beam is mono-energetic.

3. Calculate the effect of beam hardening on the CT image of a disk.

4. For the following sample, show (a.) the projections and (b.) the filtered projections

4. A sinusoidally modulated x-ray image is recorded by a one-sided screen film system as shown below.  Find the recorded S/N as a function of frequency, where the signal is the sinusoidal component and the noise is the average background.  On average the screen produces l photons per x-ray photon, t of which are transmitted to the emulsion where r are recorded.  The pixel area of the film is much smaller than the system resolution.  Neglect any critical angle effect between the screen and the film.

x-ray photon number as a function of z = n0 (1+cos(2 π k z)).

5. Write a program that calculates the Radon transform of an object function, then Fourier filters the projects, and finally reconstructs an image via back projection.

# Text boxes

z

d

screen

µ

d

screen

µ

film

z

film