MFP SAFETY PRECAUTIONS

Ortiz Nanomechanics Lab : 13-5037

1. PHOTODIODE AND LASER KNOBS : Please be sure not to push them beyond their range of motion. They

are quite sticky at the ends and may get stuck or the belt may come off.

2. FLUIDS. Although there is minimal danger if fluids leak down into the base, please be careful when inverting the head and keeping the tip wet. If some of the fluid leaks back into

the "volcano" passing through the tip holder / laser

focusing lens into the depth of the volcano-it can damage all

of the main MFP components.

3. WIRE CONNECTING HEAD TO BASE: Be careful not to twist or stretch it too much when changing

samples/tips.

4. LASER FOCUSING LENS : Please do not use the laser focusing lens, there is no safety guard on it [Summer, 20000].

5. BUNGEE TRIPOD : Please do not use with MFP or anything similar, there is a pretty big danger of it becoming unbalanced and falling off.