# Underwater energy (uwenergy@mit.edu)

## Goals

### Macro scale project

#### Enough power to light up an abandoned oil rig (10-100X 100W light bulbs = 10-100kW)

#### Extreme reliability (~ 10 years)

#### Completely autonomous

#### Easy to deploy

### Micro scale project

#### To power electronic fish tags by capturing the kinetic energy of an animal swimming through the water

#### Sensors on fishes

## Background

### Price of electricity

#### US average in 2003 is about 8 cents per kWh (1kWh = 3.6MJ), 12 cents in MA

##### http://www.eia.doe.gov/neic/brochure/electricity/electricity.html

### Suggested reading

#### Energy Numbers

##### http://www.ocean.washington.edu/courses/envir215/energynumbers.pdf

### Known failure modes

#### Corrosion: submarine lifespan is 30 years with overall reconstruction every 3-5 years

## Alternative energy sources

### Wind

#### 40% wind-to-mechanical efficiency

#### 85% mechanical-to-electrical generator efficiency

#### 35% overall efficiency

##### http://www.uaf.edu/coop-ext/publications/freepubs/EEM-01352.pdf

#### Power output of 2MWe (Mega Watts electrical, unit of output electric power), grouped into farms of 200MWe

#### 25% load factor (capacity factor?)

#### 4-25m/s wind speed, max output at 12-25m/s

#### 50m long blades, foundations require hundreds of cubic meters of reinforced concrete

##### http://www.uic.com.au/nip38.htm

### Light

#### Photovoltaic cells: 15% capacity factor, 15% light-to-electric efficiency

##### http://www.uaf.edu/coop-ext/publications/freepubs/EEM-01352.pdf

### Fossil fuels

#### Conventional power plant thermal efficiency: 30-40%

##### http://www.uaf.edu/coop-ext/publications/freepubs/EEM-01352.pdf

## Energy sources:

### Types of currents

#### Technical background and terminology

##### http://www.irbs.com/bowditch/pdf/chapt09.pdf

### Tidal flows

#### 2-3m/s are equivalent to wind speed over 200km/hr (56m/s)

#### 1MWe turbine reduces from 60m in wind to 20m in water

##### http://www.uic.com.au/nip38.htm

#### Sergius Narrows, AK, 6kt = 3m/s (1kt=0.514m/s), 12hr period

#### Gillard Pass, BC, 7kt, 12hr period

#### Gorge-Tillicum, BC, -7kt, 24hr period

#### Nakwakto, BC, 10kt, 24hr period

#### Sechelt, BC, 11kt, 24hr period (?)

#### Seymour, 11kt, 24hr period (?)

##### http://www.sailwx.info/tides/tidemap.phtml

### Characterization of surface ocean currents

#### Accessible from oil rigs (depth, speed?)

##### http://oceancurrents.rsmas.miami.edu/index.html

### Oceanic currents (oceanic circulation)

#### Accessible from oil rigs (depth?)

#### South equatorial current, 2.5kt = 1.3m/s, east coast of South America

#### Gulf Stream (Florida current), 2-4kt = 1-2m/s

#### Kuroshio Current, 3mph = 1.3m/s, Japan

##### http://www.irbs.com/bowditch/pdf/chapt32.pdf

## Alternative power generators

### Aquantis

#### Colvos passage, Florida (check)

#### 30m horizontal axis turbine

#### Nine turbines span 500m, 100m deep

#### 750kW per turbine X 9 = 6.75MW = 13GWh/yr

#### 22% capacity factor

#### Turbines rated at 1.6m/s

#### Production of energy from hr 3 to hr 10 (0.6m/s minimum) out of 12 hr half period; max speed at 1.6m/s; total power is 35.4MWh/day

#### Usable flow is 14,000 cubic meters per second

#### Cost (operation & maintenance) 2-3 cents per kWh

##### http://iere.org/energy/Vashon-Summary.pdf

### Blue Energy Power System

#### 7m ducted vertical axis turbine, 250kW X 31 = 7.75MW

##### http://egsa.org/powerline/plarticle.cfm?article=60

### Abacus Controls

#### 3m dual horizontal axis turbines, 90kW X 60 = 5.4MW

##### http://iere.org/energy/Vashon-Summary.pdf

### Marine Current Turbines

#### First offshore (3km, check!) tidal current turbine

#### Operating now for two years

#### 300kW in 5.5kt (2.7m/s)

##### http://www.marineturbines.com/mct_text_files/Press%20Release%20MCT%2016%20May%2003%20V2.0.pdf

### Upper bound: Conversion of water speed into power

#### Momentum flux = integral (n dot ρ V) V dA

#### Average energy = ½ ρ g (A squared)

#### ρ (U squared) = momentum per area?

## Design of oscillatory systems

### Advantages

#### No seals

### Problems

#### Fatigue

## Design of rotary systems

### Advantages

#### Ease of design

#### High energy efficiency

### Problems

#### Failure of seals (reliability)

## People

### Alexandra Techet

#### Email ahtechet@mit.edu

### Jose Oscar Mur-Miranda

#### Office at Olin 781-292-2544

#### Personal cell 617-314-0515

#### Email jomm@olin.edu

### Tadd Truscott

#### Lab 617-324-7157

#### Cell 339-927-8002

#### Home 781-648-1520

#### Email truscott@mit.edu

### Erik Dawe

#### Lab 508-289-2448

#### Home 508-495-3312

#### Email edawe@whoi.edu

### Johanna L. Mathieu

#### Email jmathieu@alum.mit.edu

#### Email jmathieu@gmail.com