## Slide 1: IFU for Spectropolarimetry Applications
Haosheng Lin, Tom Schad,
Institute for Astronomy, University of Hawaii
Yukio Kasukawa
National Astronomical Observatory of Japan
Kiyoshi Ichimoto
Kyoto University

## Slide 2: High Resolution (spatial, spectral, and temporal) Imaging Spectroscopy & Polarimetry He I 1083 nm line

## Slide 3: Outline
Spectropolarimetry in Solar Physics
Brief review of Stokes Polarimetry
How are solar IFU different from nighttime IFUs?
Short history of Solar IFUs
IFUs optimized for solar observations
Fiber Optics for Spectropolarimetry
Current Instrumentation Projects

## Slide 4: Spectropolarimetry in Solar Physics
Spectropolarimetry is the most important tool for the study of solar magnetism in modern solar physics

## Slide 5: Solar Magnetism and Polarization
Most of the spectral lines from the solar atmosphere are polarized through several polarization mechanisms
Zeeman Effect
  Polarized radiative transfer of Zeeman sensitive spectral lines in a magnetized, optically thick atmosphere
(Classical) Hanle effect in upper photosphere, chromosphere and corona
  Scattering polarization of spectral lines in the weak field regime in a magnetized, optically thing atmosphere
Saturate Hanle effect in upper photosphere, chromosphere and corona
  Scattering polarization of spectral lines in the strong field regime in a magnetized, optically thing atmosphere

## Slide 6: Polarized Spectra of He I 1083 nm Line Region
Hanle Effect Polarization
Zeeman Effect Polarization
Zeeman Splitting

## Slide 7: Stokes Polarimetry – A Brief Overview

## Slide 8: Definition of Stokes Parameters

## Slide 9: Dual-LCVR Polarimeter
Modulation Sequence…
Demodulation Formulae
Polarization Modulator
Polarization Analyzer

## Slide 10: Time-Differenced Polarimetry
Typical polarimeters measure I‘1, I‘2, I‘3, and I‘4 sequentially in time…
Seeing and evolution of solar features will results in errors in polarization measurements…

## Slide 11: Errors in Polarimetry
Time-Differenced Polarization Measurements:
  Stokes parameters are obtained from differencing two polarimeter measurements obtained at different time…
Source of Spurious Polarization Signals in time-differenced polarization measurement
  large intensity and velocity gradient across the field of view in the presence of seeing or instrument induced image motion
  Fast evolving solar features
Spurious polarization-like signals can be minimized with
  dual-beam polarimetry
  kHz modulation – not possible with large format FPAs…

## Slide 12: Dual-Beam Polarimeter
Ip = I - Q
Is = I + Q
Wollaston Polarization Beam Splitter

## Slide 13: Quiet Sun Magnetic Fields: Are they real?
a
Anti-symmetric Stokes Q?
Anti-symmetric Stokes U?
Are these weak polarization signals real?
I
Q
U
V
V ~ 10-3 Ic
Slit

## Slide 14: Quiet Sun Magnetic Fields: Are they real?
a
I
Q
U
V
V ~ 10-3 Ic
Slit

## Slide 15
Seeing induced spurious signals are reduced when the two beams are combined…to reveal true solar polarization signals

## Slide 16: Dual-Beam Polarimetry with Fibers?
Standard ptical fibers scramble polarization signals as the EM waves are guided through the fibers…
  Billions of stress induced, randomly oriented birefringent waveplates change the output polarization states of the waves…
Dual-beam polarimetry can be performed BEFORE the fiber arrays
  Requires twice the number of fibers for the same field of view…
  ESPaDOnS!
Polarization maintenance fibers can preserve S & P polarization states…and can be used for dual-beam polarimetry!

## Slide 17: Requirements of Solar IFUs
Spectral Resolution & Spectral FOV
  R ~ 300,000  small core fiber
  Δλ ~ λ/1,000
  nλ ~ 200
Spatial Resolution & Spatial FOV
  Diffraction limited over a substantial FOV
  E.g., 0.03” pixel over 30” FOV
  nx x ny ~ 1,000 x 1,000
  Need vary large format IFUs
  Need many spectrographs and cameras
  Need to maximize no. of fibers per spectrograph
Preserve polarization  polarization maintenance fibers
  Preserve Ex and Ey of light guided through the fibers

## Slide 18: Fiber Optics in Solar Astronomy
A Brief History

## Slide 19
Year | 1985 | 2003 | 2004 | 2009 | 2013
Instrument | Haleakala Stokes Polarimeter | OFIS | BiFOIS-1K | SPIES-2K | BiFOIS-4K
No. of Imaging Elements | 1 | 128 | 1,024 | 2,048 | 3,840
Input Array | 1 | 16 x 8 | 32 x 32 | 64 x 32 | 64 x 60
Output Array | 2 | 2 x 64 | 2 x 512 | 8 x 256 | 4 x 960
Array Construction | Conventional fibers | Conventional | Stacked Ribbon | Conventional fibers | Stacked Ribbon
Fiber | Fujikura | Fused Silica | Borosilicate | Fused Silica | Borosilicate
Core/Cladding [um] | 80/125 | 50/125 | 38 x8/40x10 | 50/125 | 38x8/40x10
Imaging Element Size [um] | Φ80 | Φ160 | 40 x 40 | Φ160 | 40 x 40
Imaging Element Filling Factor | 100% | NA | 78% | NA | 78%
References | http://adsabs.harvard.edu/abs/1985SoPh...97..223M | http://adsabs.harvard.edu/abs/2004ApJ...613L.177L | http://adsabs.harvard.edu/abs/2006SPIE.6269E..18L | http://adsabs.harvard.edu/abs/2012SPIE.8446E..1DL | SPIE 2004 in press

## Slide 20: Dual-Beam Polarimetry With Conventional Fibers
Haleakala Stokes Polarimeter
ESPADons
Camera 1
Fiber 1
Polarization Analyzer
(e.g., Wollaston) Filter out U and V states and separates Ex and Ey beams
Polarization Modulator (e.g., λ/3 retarder) encodes polarization measurements in the Ex and Ey components of light
Camera 2
Spectrograph

## Slide 21: Conventional Fiber-Optic IFUs
OFIS: 128 fibers, 16 x 8 -> 2 x 64
SPIES-2K: 2,048 fibers, 64 x 32 -> 8 x 256

## Slide 22: OFIS: A True Imaging Spectropolarimeter
The coherent optical fiber-bundle rearrange the 2-dimensional image sampled by the 16 × 8 input array to two linear array (2 × 64 ). The two linear arrays act as the slits of the spectrograph, thus allowing for the simultaneous recording of the spectra from all the field points in the 2-D image plane.
Fiber Bundle
Collimator
Echelle Grating
Camera Lens
NICMOS3 IR camera
NICMOS3 IR Camera
16  8 => 2  64 optical fiber-bundle
160  308 mm, 79 lines/mm echelle grating with 63.5 blaze angle
f = 800 mm,  = 150 mm (F/5.3) collimator and camera lens

## Slide 23: SOLARC – Solar Observatory for the Limb and Active Region Coronae J. R. Kuhn
LCVR Polarimeter
Input array of fiber optics bundle
Re-imaging lens
Prime focus inverse occulter/field stop
Secondary mirror
Primary mirror
SOLARC and its dome on the summit of Haleakala, Maui.
Optical Configuration of SOLARC and OFIS
50 cm aperture off-axis gregorian telescope
No secondary mirror and spider structure in the optical path for coronagraphic performance

## Slide 24: Sample Coronal Emission Line Spectra from OFIS
  One 64-fiber column illuminated
  16 × 4 pixels area coverage
  Two 64-fiber columns illuminated
  16 × 8 pixels area coverage
Fe XIII 1074 nm line

## Slide 25: Circular Polarziation
Best spectral line for coronal B measurement
  Fe XIII 1075 nm
Amplitude of CP
  Solar Maximum: ~ 10-3
  Solar Mimumum: ~ 10-4
With a 50-cm coronagraph on the ground
  20” pixel
  30 × 10-6 Ic scattered light
  1 hr integration time
  3 G (3 ) sensitivity @ 1.1 Rsun

## Slide 26: Coronal Magnetogram, April 6, 2004
Contour plot of the line-of-sight magnetogram over-plotted on the SOHO/EIT FeXVI 284 A image. The contours are 5G, 3G, and 1G.
Transverse field orientation
Longitudinal Field Strength

## Slide 27: Circular Polarziation, Low Activity Period

## Slide 28: SPIES-2K Fiberguide Industries
64 x 32 – 8 x 256

## Slide 29
32
64

## Slide 31: BiFOIS-1K
Birefringent Fiber-Optic Image Slicer

## Slide 32: BiFOIS Design Goals
Increase FOV coverage per spectrograph
  Use fibers with size comparable to camera pixel size
Increase telescope – fiber coupling efficiency
  Use thin cladding fibers with large core filling factor
Simplify array fabrication process and reduce fabrication cost
  Use fiber ribbons as the building block of the array
  No microlens array
Preserve polarization for dual-beam spectropolarimetry
Ribbon constructed with rectangular fibers…

## Slide 33: Dual-Beam Polarimetry Through PM Fibers
Camera 1
PM Fiber
Polarization Analyzer
(e.g., Wollaston) Filter out U and V states and separates Ex and Ey beams
Polarization Modulator (e.g., λ/3 retarder) encodes polarization measurements in the Ex and Ey components of light
Camera 2
Spectrograph

## Slide 34
Small, thin clad fiber ribbon appears as continuous line on camera
  Efficient use of camera pixels
Large aspect ration introduces geometric birefrigence
  Dual beam spectropolarimetry is possible through the fibers
Fiber ribbons as building blocks of IFUs
  Reduces complexity and fabrication cost of IFUs

## Slide 35: BiFOIS Prototype Input and Output Arrays Collimated Holes
Output Array:
2 x 20.48 mm x 0.04 mm linear array,
equivalent to two continuous long slits.
Input Array:
32 1.280 mm x 0.040 mm ribbons,
equivalent of 32 x 32 square array with 40 um pixel size.

## Slide 36: First Demonstration of Dual-Beam Spectropolarimetry through Fibers
I
Q
U
V

## Slide 37: BiFOIS Prototype Time Sequence
10” x 10” FOV
0.3”/pixel sampling with low-order AO
10 second time resolution
15 minutes

## Slide 38: Problems…
Curved ribbons
  Is it possible to build science-grade IFUs with this method?
Thin Cladding Design
  Inter-fiber crosstalk – especially in IR?
Borosilicate Fiber
  Transmission loss?
Modal Noise?
Polarization Properties?

## Slide 39: BiFOIS-4K
3,840 pixels (15,360 fibers) Birefringent Fiber-Optic Image Slicer

## Slide 40: Development of Better Ribbons
Rectangular Fiber Ribbon for BiFOIS |  | 
Fiber Material | Borosilicate, ~ 800 dB/km attenuation | 
Elemental Fiber | core | Core+cladding
 | 38 um x 8 um | 40 um x 10 um
Filling Factor | ~ 80% | 
Building Block | 1 x 128 ribbon, 40 um x 1.28 um | 
Fiber Length | 10 cm | 

## Slide 41: Array Construction Process

## Slide 42: BiFOIS-4K
Much Improved Imaging Array!
Two stacks of 60 ribbons
64 x 60 imaging pixels
95% yields

## Slide 43: 4-Slit Exit Array
4 x (1 x 960) pixels linear arrays

## Slide 44: Segmented Linear Array Etched Silicon Fiber Channel Chips

## Slide 45: Detailed Characterization of BiFOIS
Transmission Loss
Inter fiber Crosstalk
Focal Ratio Degradation
Modal Noise
Polarization Maintenance
Full Polarization Muller Matrix

## Slide 46: Fiber Attenuation
Borosilicate (thick cladding)
  < 1,000 dB/km -> 0.1 dB/10 cm -> 97%/10 cm
1580 nm
420 nm
BIFOIS Material
Attenuation [dB/km]

## Slide 47: BiFOIS Broadband (400 – 1000 nm) Transmission Loss Impurity scattering + leaky cladding
Measure total transmission loss with “Replacement Method”
  Measuring the output intensity of two fibers with different length, given identical input condition…
T10 ≥ 75%
  This figure includes 8% reflection at the two air-glass interfaces…
With perfect AR coating,
T10 ≥ 83%

## Slide 48: Impact on Instrument Efficiency In comparison with etched glass slit
BiFOIS photon throughput is 65% of etched glass slit with the same slit width
      ENoAR = 0.75 × 0.8 (filling factor) / 0.92 = 0.65
      EAR = (0.75+0.08) × 0.8(filling factor)/1. = 0.66
IFU significantly reduces the number of scan steps to cover a meaningful FOV.
  For a 64 x 64 IFU, the IFU instrument is 0.65 × 64 = 41 times faster than a scanning long-slit spectropolarimeter to obtain a N x 64 image with the same sensitivity.
  We can tolerate a moderate level of efficiency loss from the fiber!

## Slide 49: Filling Factor Loss Mitigation
A weak cylindrical microlens array can be used to increase the filling factor to near 100%...
    For a 64 x 64 IFU, the IFU instrument is 0.75 × 64 = 48 times faster than a scanning long-slit spectropolarimeter to obtain a N x 64 image with the same sensitivity.
8 um
10 um

## Slide 50: Inter-Fiber Crosstalk via Evanescent Wave Coupling
Evanescent wave arises from the boundary condition that the EM wave must be continuous at the boundary between two media…
  EW decays exponentially
  Typical penetration depth is a few hundred nm…
  Industrial ‘rule-of-thumb’ for cladding thickness is ~ 10 λ
Evanescent Wave

## Slide 51: Crosstalk Test configuration Courtesy Y. Katsukawa, NAOJ
Pin hole
(ϕ5 µm)
camera
Lamp
Stop
(5-15 mm)
~200 mm
~260 mm
~185 mm
Interference filter
BP 10 nm
camera lens
fiber sample
(straight, L=100 mm)
camera lens
Pin hole
(ϕ5 µm)
Lamp
Stop
(5-15 mm)
~200 mm
~260 mm
~185 mm
Interference filter
BP 10 nm
camera lens
Measurement of the input beam profile
Measurement of the output beam profile
At each wavelength, the pinhole position is adjusted along the optical axis to make the beam size minimum.
The position of the fiber sample is adjusted laterally to make the output beam brightest.
camera

## Slide 52: Inter-Fiber Crosstalk 500 nm (BP 10nm) Courtesy Y. Katsukawa, NAOJ
Stop:
ϕ5mm
(F/37)
Stop:
ϕ15mm
(F/12.3)
Stop:
ϕ10mm
(F/18.5)
Input
Output
Input
Output
Input
Output

## Slide 53: Inter-Fiber Crosstalk 1000 nm (BP 10nm) Courtesy Y. Katsukawa, NAOJ
Stop:
ϕ5mm
(F/37)
Stop:
ϕ15mm
(F/12.3)
Stop:
ϕ10mm
(F/18.5)
Input
Output
Input
Output
Input
Output

## Slide 54: Analysis Courtesy Y. Katsukawa, NAOJ
The input beam profiles are fitted with a Gaussian function
  The pixel scale of the camera is 4.4 μm.
The output beam profile are fitted with Gaussian x Sin2.
  Based on the Sin2 fitting, we derive pixel scale by assuming the interval of the dark lanes is 10 μm.
FWHMs of the Gaussian function are evaluated and compared between input and output beams at each wavelength.

## Slide 55: Inter-Fiber Crosstalk Results Courtesy Y. Katsukawa, NAOJ
The size of the output beam monotonically increases as a function of the wavelength while the size of the input beam does not change so much in the case of F/12.3 and F/18.5.
  In the case of F/12.3 and F/18.5, the size of the input beam does not depend on the wavelength because the beam profiles are primarily determined by aberration of the camera lens. The influence of the diffraction is very small.
  The degradation of the beam size is not so significant in the visible wavelength range (500 nm, 580 nm, and 633 nm).
  The degradation is significant in the IR wavelength range (800 nm, 900 nm, and 1000 nm), which indicates significant leakage to adjacent fibers (crosstalk) at these wavelengths.
In the case of F/37, the sizes of the input beam and output one are not so different. The large F may help to reduce the crosstalk.
  In the case of F/37, the size of the input beam monotonically increases as a function of the wavelength because of the diffraction effect.

## Slide 56: Focal Ratio Degradation Measurement
Illuminate the fiber using SCL beam with variable F/#
Measure the exit beam width at three distances from the fiber
  Precise distance to the fiber is difficult to obtain…
Pick-up fiber for photometer
Supercontinuum laser collimator
Motorized liner stage

## Slide 57: BiFOIS Broad-Band Focal Ratio Degradation

## Slide 58: BiFOIS Broad-Band Focal Ratio Degradation
BiFOIS output is a constant F/15 (FWHM) for input slower than F/30
DL-NIRSP baseline spectrograph can accommodate F/12 Gaussian beam input with 100% ray through…
  Pei’s presentation

## Slide 59: Modal Noise Direct BiFOIS Spectral Image
Only dark subtraction…
No apparent modal noise contamination…

## Slide 60: Comparison with FTS Solar Spectrum
No apparent modal noise in BiFOIS spectrum…
Black – BiFOIS spectrum, dark subtracted only
Blue – Reference FTS spectrum

## Slide 61: BiFOIS Modal Noise Estimate
Compare measured noise in BiFOIS difference images to that inferred from average intensities

## Slide 62: PM Experimental Setup
Rotate LP1 with 22.5 deg increment
Scan LP2 with 10 deg increment for each LP1 position
LP1
LP2
Fiber
Photometer/Spectrograph
Photometer/Spectrograph
Fiber
LP2
LP1
Reference
Fiber Measurement

## Slide 63: Broad-Band Polarization Maintenance
Rectangular Fiber is naturally birefringent…and preserves linear polarization in the long and short direction of the fiber core…

## Slide 64: Spectral Polarization Maintenance
Spot Check – from a small section of a ribbon…

## Slide 65: Spectral Polarization Maintenance
For all 4 ribbons
High Stress Regions?

## Slide 66: Full Muller Matrix – Response to

## Slide 67: Muller Matrix
Describes how an optical component modify the polarization of light…

## Slide 68: Polarization Maintenance

## Slide 69: U, V – Q Crosstalk

## Slide 70: BiFOIS-4K Imaging Spectroscopy Demonstration He I 1083 nm line
Developing data reduction pipeline

## Slide 71: BiFOIS-4K Imaging Spectroscopy Demonstration He I 1083 nm line

## Slide 72: Polarimetry Demonstration Fe I 1565 nm lines
Developing polarization crosstalk calibration procedure

## Slide 73: Next Step
DL-NIRSP
BiFOIS-5K Spectropolarimeter on the 4-m DKIST
In Critical Design Phase

## Slide 74: Daniel K. Inouye Solar Telescope formerly Advanced Technology Solar Telescope
4-m aperture, Off-Axis coronagraphic Telescope
Haleakala, Maui, Hawaii
Under construction since December, 2012
First Light: 2019

## Slide 75: First Light Instruments
Visible Broad Band Imager
Visible Spectropolarimeter
  350 nm – 900 nm
  Long-slit spectrograph
  3 wavelengths simultaneously
Visible Tunable Imager
  Fabry-Perots spectrometer
Diffraction-Limited Near-IR Spectropolarimeter
  500 nm – 2,500 nm
  BiFOIS-5K IFU
  3 wavelengths simultaneously
Cryogenic Near-IR Spectropoarimeter

## Slide 76: DL-NIRSP 4,800 (80 x 60 – 5 x 960) imaging elements IFU
a

## Slide 77: Summary
New method for the construction of high-density, large-format IFUs
  Fiber ribbons simplify array fabrication process
  Thin cladding fibers allow for efficient use of camera pixels
Polarimetry through fiber optics is possible
  Short, rectangular core fibers preserve polarization states
Is it possible to build this with fused silica fibers?

## Slide 78: Thank You!