## Slide 1
The VIRUS 35k fiber system:
design, fabrication, characterization, and data reduction
Gary J. Hill
McDonald Observatory, University of Texas at Austin
Andreas Kelz
Leibniz Institute of Astrophysics Potsdam (AIP)

## Slide 2: Overview
Motivation
  Wide field 3D spectroscopic surveys
  HETDEX and VIRUS
Design overview of VIRUS – 35k fibers on sky
  Spectrograph
  IFUs
  Deployment
IFU Development and testing
  Design prototyping – VIRUS-P and evolution of VIFU design
  Lifetime testing
  Final production design
IFU production
  Requirements flow down
  Vendor relationships
Acceptance testing and characterization
  Acceptance testing
  Characterization
System testing
  Image quality
  Fiber throughput and uniformity
Data reduction and analysis
  The science requirements
  Cure
  Experience with VIRUS-P
Deployment Plan
Replicated fiber-fed spectrographs in the broader context

## Slide 3: HET upgrade, VIRUS, and HETDEX
Hobby-Eberly Telescope Dark Energy Experiment is the principal motivator
  Blind survey of more than a million emission-line galaxies up to redshift z=3.5
  Constrains expansion history of the Universe
  Direct detection on dark energy at z~2.5 even if a cosmological constant
  Aims to tell if dark energy evolves
Upgrade of HET to 22 arcmin FoV and 10 m pupil
  New corrector and tracker
Deployment of Visible Integral-field Replicable Unit Spectrograph (VIRUS)
  Blind spectroscopy of 55 sq. arcmin per observation with 34,944 fibers
  The first highly-replicated instrument in optical astronomy (156 channels)
HET will be transformed into a hugely powerful survey instrument
Hill et al Proc SPIE 9145-5 (2014)
Good et al Proc SPIE 9145-156 (2014)
HET in 10 months time
New corrector and tracker
VIRUS enclosures
VIRUS IFUs

## Slide 4: Motivation
Primary motivation is HETDEX
  Blind spectroscopy of LAEs over 420 sq. degrees with 1/4.5 fill-factor
  Combination of light gathering power of 10 m HET and replicated IFS
    Enormous AΩ needed for this problem
  VIRUS has as many pixels as DECam and 35k fibers, each 1.5”
VIRUS IFUs have ~50x more fibers than typically deployed before
  in e.g. Hermes and other fiber-fed instruments with ~400-1000 fibers each
  Next generation of fiber MOS (WEAVE, 4MOST) ~2k fibers, though targeted
Wide field 3D spectroscopic surveys
  Up till now all targets have continuum counterparts
    or are discovered in very expensive narrow band surveys and then followed-up with targeted spectroscopy
  Blind wide field IFS is expensive but has unique applications
    VIRUS is the first instrument to be able to do this over 100s of sq. deg.
    VLT MUSE has very different design but similar power and can go very deep over small fields

## Slide 5: VIRUS IFU Design Overview
Brian Vattiat, Svend Bauer, Hanshin Lee, Jeremy Murphy, Richard Savage, Sarah Tuttle

## Slide 6: Basic properties of the IFU
VIRUS IFUs had to be fiber based….
  HET couldn’t carry weight of the spectrographs
  Learned lesson with HET LRS… fiber azimuthal scrambling is crucial when the pupil illumination is variable
… and had to be simple and efficient
  Design had to be replicable on large scale by multiple vendors to get through the work
  Direct coupling of light into fibers is not only efficient but allows use of catadioptric spectrograph (crucial for 350 nm) without great losses
  Traditional coupling with lenslets swaps the image and pupil planes and has coupling losses due to lenslet imperfections, alignment errors, and diffraction
When surveying area there is no advantage to lenslet fill factor at same f/# into the fibers
Settled on a simple configuration with 1/3 fill factor of the fiber cores
  The IFUs are dithered very precisely to fill in the area
  This introduces a mechanical engineering complexity but is optically simple and has high efficiency

## Slide 7: VIRUS spectrograph
VIRUS is a simple spectrograph replicated on large scale
  156 channel fiber-fed IFS in 78 units placing 35k 1.5” dia fibers on sky (266 μm core)
  350-550 nm coverage and R~700
  125 mm beamsize to accommodate catadioptric camera needed for UV coverage
  No moving parts
VIRUS protoype (Hill et al 2008) has been used at McDonald 2.7 m for 7 years
  Used for HETDEX pilot survey (Adams et al 2010, Blanc et al 2010)
  Proved the optical design, principles of the mechanical design, and the data reduction software
Lee et al. Proc SPIE 7735-140 (2010); Hill et al. Proc SPIE 9147-25 (2014)
930 l/mm VPHG
Collimator mirror
Camera mirror
Flat mirror
Field flattener & CCD
Corrector

## Slide 8: VIRUS hardware components
Each unit has two channels fed by 448 fibers
Fiber IFU production led by AIP - Kelz et al Proc SPIE 9147-269 (2014)
Collimator production led by TAMU
  Marshall et al Proc SPIE 9147-143 (2014)
Grating production led by UT, purchased by TAMU
  Chonis et al Proc SPIE 9151-53 (2014)
Camera production and integration led by UT Austin
  Tuttle et al Proc SPIE 9147-26 (2014)
Spectrograph integration and alignment led by UT Austin
  Lee et al Proc SPIE 9151-138 (2014)
Camera
Collimator
Cover
IFU slit assembly
Camera
Detector electronics
>15,000 parts (not incl. fasteners)
Many mechanical parts produced by Oxford Physics and Göttingen (IAG)

## Slide 9: IFU design overview
18, 20, 22 m lengths
  448 fibers per IFU (266 μm core, high OH for λ ≤ 720 nm)
Input has 1/3 fill packing of cores
  IFUs are dithered through three positions to fill in the area
Design: Svend Bauer, AIP & Brian Vattiat, MDO

## Slide 10: VIFU Input head anatomy
Custom Aluminum conduit with PVC sheath by Hagitek Japan for weight savings
Braided Kevlar sleeve, glued at head, tensioned at slit end after assembly
Precision alloy hole block to set fiber positions by Euromicron
Many parts by IAG (Göttingen)
Not shown: black mask and input lens

## Slide 11: VIFU slit end anatomy
Conduit clamp &
length adjustment
Kinematic mount plate
Not shown: cylinder output lens & mask
Lens & mask holder
Groove block
cap

## Slide 12: VIFU fiber mapping
Pin
Fiber 1
Fiber 448

## Slide 13: Contributors to FRD
There is an allowance on FRD built into the VIRUS design
  f/3.65 input from new wide field corrector that is optimized for fibers
    Telecentric to high accuracy over 22 arcminute field of view
  Collimator accepts f/3.47
  still need to minimize all FRD contributors to reduce loss of resolution and sensitivity
FRD contributors are both internal and external
  Modern fiber shows very little radial scrambling of modes at f/3.65
  FRD generation primarily at insertion and exit
    Immersing polished fibers at input and exit mends most of the FRD and allows AR coating of a macro optic
  Bend radius or other stress
  Ageing (micro-damage)
  Geometric/aiming effects

## Slide 14: Contributors to FRD
Entrance contributors to FRD
  Quality of polish and avoiding stress
  Tilts of individual fibers
  Wedge on input face
  Aiming of IFU axis wrt chief ray as function of field position
Exit contributors to FRD/light-loss
  Quality of polish and avoiding stress
  Aiming of fibers/wedge translates pupil and loses light (not FRD per se)
Testing shows FRD causes preferential propagation of light into slower f/# modes in central obstruction rather than a faster beam
  This matters for VIRUS due to detector obstruction

## Slide 15: IFU Design Development and Testing
Svend Bauer, Brian Vattiat, Jeremy Murphy, Josh Adams, Guillermo Blanc, Richard Savage, Emil Popow, Martin Roth, Niv Drory, Phillip MacQueen, Joe Tufts, Karl Gebhardt, Mike Smith, John Good, Hanshin Lee, Sarah Tuttle

## Slide 16: Mitchell Spectrograph (VIRUS-P) prototype and HETDEX Pilot Survey (HPS)
6/9/2010
Prototype to test performance and inform production, including IFU
VIRUS-P has been in regular science operation since Oct 2006
  Performance meets HETDEX requirements
  Provided the cost basis for replicating instrument
  Platform for software development
2 year Pilot Survey for HETDEX (HPS)
  It is rare to be able to test the ideas end-to-end before starting a big project
  Adams+ (2010); Blanc+ (2010)
VIRUS Prototype on 2.7 m Smith Telescope
247 fibers

## Slide 17: Example Data
3450-5850 Å spectral range
  resolution of 5 Å FWHM (R~900)
  Data binned 2x in spectral dimension
6 position dither pattern ensures good field coverage
  4.1 arcsec dia fibers on 2.7 m (200 μm core)
Three 20 min exposures at each position cover 3.3 sq. arcmin
2 hr of effective exposure time per field in HPS

## Slide 18
VIRUS data reduced with two independent pipelines
Vaccine (U. Texas) and Cure (USM/MPE Munich)
5σ flux limit of ~6x10-17 erg/s/cm2 for a point-source and unresolved line
Example Data

## Slide 19
LYMAN ALPHA EMITTERS
Low-z GALAXIES
HPS example galaxies
Adams et al (2010)

## Slide 20: VIRUS-P as IFU test bed - degradation of VP2 IFU
The VP2 cable was 15 m long and was used at HET as well as at the Smith Telescope
  Each month the instrument was dismounted and the IFU coiled as shown
  After 3 years of operation transmission decrease was seen in 18 of 246 fibers
    All in the corners – very strong “explosive” FRD (up to 85% loss)
  Diagnosed as due to local stress at the head, caused by repeated twisting the fibers
  Clearly demonstrated with FRD test bench at UT
VIFU handling protocol now avoids any twisting (and V-P IFU was replaced)
  Ramifications for “orbital style fiber positioners that twist the fiber?
= bad

## Slide 21: Lifetime testing
Simulation of 9.4 years of motions on the HET in order to validate the cable design
  ~100 fibers monitored for FRD in accelerated test over 4 months of movement (173 km of total travel)
    Ring test with angle equivalent to f/3.65
  Fiber routing mimicked HET fairly well, a hexapod and linear stage provided the motion
  3 different tracks, wide range of speeds (0.77 to 120 mm/s), 24 hour operation
  Murphy et al Proc. SPIE 8446, 84465F (2012)
Purpose
  Study the effect of motion on the VIRUS fiber bundles
  Understand the requirements on the calibration systems based on how the fibers pass light while in motion
  Monitor fiber breakage and changes in transmission and FRD over the lifetime of the fibers.
Test setup in subterranean rail-gun range at CEM

## Slide 22: Lifetime testing
Simulation of 9.4 years of motions on the HET in order to validate the cable design
  ~100 fibers monitored for FRD in accelerated test over 4 months of movement (173 km of total travel)
  Fiber routing mimicked HET fairly well, a hexapod and linear stage provided the motion
  3 different tracks, wide range of speeds (0.77 to 120 mm/s), 24 hour operation
  Murphy et al Proc. SPIE 8446, 84465F (2012)
Purpose
  Study the effect of motion on the VIRUS fiber bundles
  Understand the requirements on the calibration systems based on how the fibers pass light while in motion
  Monitor fiber breakage and changes in transmission over the lifetime of the fibers.
Test setup in subterranean rail-gun range at CEM

## Slide 23: Methodology
Back-to-back frames are divided.
Left frame: No significant change in the behavior of the fibers.
Right frame: FRD due to motion of the fibers is apparent.
Above: Analysis of the divided frames gives us a handle of both the frequency and severity of the effect. Below: the movement of the fiber at the exit of the conduit was also closely monitored.
Notes: There’s some animation in this frame. It’s probably worth explaining that the two plots show the cross-section through many frames. Each division gets it’s own line. There are two sets of lines because I took two ‘strips’ through the divided frame. A strip of 31 pixels wide was median-combined, when smoothed with a 51 pixel wide box car. These smoothed curves are what’s plotted. Both sets of lines were shifted from 1.0 just for plotting purposes. Notice that even the largest deviations are at 1.0%, no more. This was true for virtually all of the tests.
The first strip plot is of the Fracker and lower stage off. The second plot shows a couple events, but mostly a steady state situation. This was not the standard case for the tests. In side 7 I have included a figure showing what the data looked like while things were in motion. I thought the plot showing just single events that stood out would be easier for folks to understand. But, you can swap in the other figure, if you prefer.

## Slide 24: FRD transients most noticeable at extremes
19k points over several days

## Slide 25: Detailed FRD testing
Measurements of 17 fibers made on test bench after lifetime test show degradation compared to measurements before
  Results are wavelength independent
  Still have 90% of light captured by collimator,
    but other FRD effects will also add to the loss
  Hence expect ~5% overall loss over lifetime of instrument due to this effect
VIRUS accepts f/3.47
HET is f/3.65
Central obstruction is f/8
Before lifetime test
After test

## Slide 26: Lifetime testing results
The fiber bundle went through a period of settling where the fiber conduit stretched by 3 to 4 cm, stressing the fibers at the exit
  Settling stopped after a week and no further significant settling was seen
  Led to change in conduit design and protocol to monitor the slit box at HET
Clear changes in fiber behavior during motion were detected
  No major FRD variations during “track” but transient FRD events at certain points at slew rate (~1%, still at very low level so can calibrate during slew)
Cable design validated, all test fibers survived
  6/316 viable fibers broke (< 2%) most likely in initial settling
Clear indication of increase in FRD in detailed measurements of 17 fibers on test bench, comparing before and after testing
  Attributed to accumulation of mechanical micro-damage over the duration of the test, but no direct physical evidence for this

## Slide 27: Final Production design
Informed by experience with VIRUS-P and the lifetime test, the changes for production were fairly minor
  Change to custom Aluminum conduit to save weight (100 kg each side)
Main issue was axial pumping of fibers within the conduit
  Conduit stretching after deployment can cause fibers to become highly stressed or broken at exit
  Mitigated by tensioning the Kevlar sleeve to take up the axial compliance of the conduit
    After doing this, the composite conduit has the CTE of Aluminum
    Tests on HET tracker in Austin showed no axial motion
  Addition of clamp at slit pan to adjust the conduit length allows fine tuning in the field if any changes are observed
Avoiding twisting of the fibers
  Ensure that the routing off the telescope is as simple as possible
  Keep the conduit spooled during handling and take care when unspooling during installation

## Slide 28: IFU Production
Hanshin Lee, Brian Vattiat, Svend Bauer, Thomas Jahn, Dionne Haynes, Christian Haubnitz-Reinke, Harald Nicklas, Heiko Anwad

## Slide 29: Requirements flow-down
Science requirements flow down to technical requirements on FRD, fiber transmission, # broken fibers, etc
  Ultimate metric is level of constraint on H(z)
    => number of LAEs detected and area surveyed in 3 years
    => technical reqts on IFUs
  FRD allowance causes a 5% loss of throughput and was partitioned between the various contributors
Specifications for vendors had to be manufacturable and testable
  Many specific requirements cannot be tested after manufacture
  Adopt a process-based compliance rather than a measurement-based one
    Fiber seating, polish compared to visual examples
    Polishing prescription to avoid sub-surface damage
    External dimensions verified with gauges
  Extensive acceptance testing protocol

## Slide 30: Internal fiber transmission requirement
Chart: Transmission of UV 265/292 P 320 Batch-Nr.: S12-302-04 P11C-1493 Measured at 13.09.2012 at IPHT Jena

## Slide 31: Geometry specifications
FRD partition and other constraints translated into measureable requirements for vendors
Input Head

## Slide 32: Geometry specifications
FRD partition and other constraints translated into measureable requirements for vendors
Output Slits

## Slide 33: Vendor relationships
An important part of the final design process was development of relationships with vendors
Transmission of requirements and discussion of technical approach
  Hard to capture all the knowledge in a requirements document
Prototyping was crucial (VIFU#)
In 2010, VIFU5 design was replicated 9 times by 3 vendors and evaluated
  Also the cable was manufactured for the lifetime test
Changes to design resulted (VIFU6) as well as addressing specific results from each vendor
Three final vendors selected after extensive evaluation
  Christian Haubnitz-Reinke Technische Dienstleistungen
    independent contractor using in-house facilities at AIP
  Ceramoptec
  Fiberware
  Fiber purchased from Leoni-Fibertech, Ceramoptec & Fiberware
AIP with contributions from UT and IAG supply a kit to the vendors
  Conduit and Kevlar
  Input head and exit slit mechanical parts
  In some cases the fiber

## Slide 34: VIRUS IFU production in steady state
Laying out fibers at AIP
Slit pans
Conduit
Output slit masks

## Slide 35: VIRUS IFU production in steady state
Completed IFU fiber cable by Ceramoptec
Laying out fibers at AIP

## Slide 36: Production and funds
Year Vendor / No. | 2012 | 2013 | 2014 | 2015
AIP | 2 | 10 | 10 | 3+3
CO | 4 | 6+7 | 15 | 
FOP | 1 | 4 |  | 
FW | 0 | 5 | 5 | 2
LFT | 1 | 0 |  | 
Total/Year | 8 | 32 | 30 | 8
Sum | 8 | 40 | 70 | 78
Black=AIP-funded, blue=MPA funds, purple=MPE co-funded, red=UT funded
Parts supplied by AIP, UT, and IAG

## Slide 37: Acceptance Testing and Characterization
Jermey Murphy, Thomas Jahn, Dionne Haynes, Justus Neumann

## Slide 38: Acceptance testing
When delivered by vendors, the IFUs are inspected for compliance with requirements
  Input head polish, flatness, wedge, protrusion
  Output slit polish, radius of curvature, wedge/rounding, packing,
  Fiber protrusion and route from conduit
  Broken fibers and fiber mapping
Then a series of tests are undertaken to characterize
  Input head fiber positions
  Fiber to fiber throughput
  FRD of selected fibers that appear substandard
Fiber polish evaluation bench

## Slide 39: Acceptance testing
Then a series of tests are undertaken to characterize
  Input head fiber positions
  Fiber to fiber throughput
  FRD of selected fibers that appear substandard
When delivered by vendors, the IFUs are inspected for compliance with requirements
  Input head polish, flatness, wedge, protrusion
  Output slit polish, radius of curvature, wedge/rounding, packing,
  Fiber protrusion and route from conduit
  Broken fibers and fiber mapping

## Slide 40: Acceptance testing
Then a series of tests are undertaken to characterize
  Input head fiber positions
  Fiber to fiber throughput
  FRD of selected fibers that appear substandard
When delivered by vendors, the IFUs are inspected for compliance with requirements
  Input head polish, flatness, wedge, protrusion
  Output slit polish, radius of curvature, wedge/rounding, packing,
  Fiber protrusion and route from conduit
  Broken fibers and fiber mapping

## Slide 41: Fiber mapping characterization
Mapping Bench
Reimaging bench mounts the input head
  Slits are back illuminated from an integrating sphere
Extremely low distortion optics verified by tests with IFU
  Comparison with fiducial IFU head maps fiber positions to common reference
  Require each fiber position on sky to be known to 0.1 arcsec (~20 μm) rms
Bench also provides measure of relative transmission of fibers, at full NA

## Slide 42: FRD and throughput
Setup at AIP is an evolution of test benches developed at AIP for PMAS and at UT for VIRUS
  Murphy et al Proc SPIE 7018-104 (2008)
A limited number of fibers are tested since effort is limited and system test provides a check
FRD evaluation bench
Input pupil and far-field image after transmission

## Slide 43: IFU System Testing
Thomas Jahn, Dionne Haynes, Ole Streicher, Maximilian Fabricius, Niv Drory, Francesco Montesano, Sarah Tuttle, Monika Rutowska, Christer Sandin

## Slide 44: System test with fiducial spectrograph
UT supplied one of the first VIRUS units to AIP for system testing
  AIP supplied LN system and light-tight enclosure
  IFU is fed as on HET
System testing is the final quality check of an IFU and includes
  Image quality (focus of IFU)
  Fiber to fiber throughput
It mimics on-sky performance so is the final check before shipping

## Slide 45: Lab data obtained with scripts
QTH + blue LED flat field
Hg+Cd emission line lamps
Plus bias and dark frames

## Slide 46: LabCure spectrograph characterization software
Spectral dimension
Spatial dimension

## Slide 47: Fiber to fiber throughput
Variations of ~few % seen between fibers
  Similar to variations seen in mapping tests at full NA
  Implies that FRD effects and fiber aiming errors are not typically coming into play

## Slide 48: Data Reduction and Analysis
Niv Drory, Maximilain Fabricius, Jan Snigula, Martin Landriau, Francesco Montesano

## Slide 49: Science to technical requirements
The problem of wide field blind spectroscopy of invisible sources where the position of the object is not known a-priori
  Most fibers looking at sky
Not entirely applicable to most fiber data
  Small IFUs are typically filled with object, not sky
  MOS devotes few fibers to sky
Lessons learned are applicable
  since the rigor required for VIRUS/HETDEX is needed on next generation of fiber instruments on large telescopes
  or for reaching very faint surface brightness limits
Strong spatial modulation in fiber spectrographs presents a challenge
  for stability of the instrument
  and calibration and data reduction methods
Cross-talk between fibers also needs to be calibrated very accurately via spatial PSF measurements

## Slide 50: Cure data reduction software
Snigula et al Proc SPIE 8451-78 (2012)
Snigula et al ASP Conf. Series, 485, 447 (2014)
MPE/USM responsible for pipeline
HETDEX will be processed with Cure
  Implemented within the astrowise environment
Have capability to simulate and process an entire VIRUS dataset
  MPE cluster with 20 cores, 64GB Memory, 200 TB disk space
Raw data volume 120 GB/night and 20 TB in three year survey

## Slide 51: Cure design principles
Each observation has 43 M resolution elements (3 x 6 min exposures)
  About 1000 of them will have signal from an emission line object (0.002%)
  Most of the rest of the resolution elements are looking at sky, except for a few 10’s of stars and galaxies (continuum sources)
There is a wealth of information on the noise characteristics of the data
  But we are truly searching for a needle in a haystack of single lines at 5-σ
Need excellent understanding of noise characteristics of every R element
  Avoid resampling (correlated noise)
  Stay in 2D (the normal generation of a 3D data cube will not work for LAEs)
  Need very stable instrument so that variations between calibrations and data are extremely small
By design, VIRUS is highly parallel in hardware and software
  VIRUS-P tested all aspects of the system with a pilot survey (HPS), including data reduction pipelines

## Slide 52: Instrument stability
Like VIRUS, VIRUS-P is gravity invariant but sees full range of ambient temperature
  V-P designed to provide a direct test of stability of the design
  Calibrations off dome were time-consuming and needed twilight flats, so only twice/night
  See shifts of spectra ~0.2 pxl / oC, so very stable, but much too great over a night
Flats at each end of night ~10%

## Slide 53: Instrument stability
Like VIRUS, VIRUS-P is gravity invariant but sees full range of ambient temperature
  Designed to provide a direct test of stability of the design
  Calibrations off dome were time consuming and needed twilight flats, so only twice/night
  See shifts of spectra ~0.2 pxl / oC, so very stable, but much too great over a night
With shifts derived from data ~5%

## Slide 54: Instrument stability
Like VIRUS, VIRUS-P is gravity invariant but sees full range of ambient temperature
  Designed to provide a direct test of stability of the design
  Calibrations off dome were time consuming and needed twilight flats, so only twice/night
  See shifts of spectra ~0.2 pxl / oC, so very stable, but much too great over a night
With improved PSF model ~2%

## Slide 55: Instrument stability
With improved PSF model ~2%
VIRUS incorporates some design changes to improve camera stability
  Instrument characterization includes detailed measurements of fiber profiles
HET Facility Calibration Unit can be deployed to quickly obtain flats and Hg/Cd lamps between observations, every 20 min., if needed
  Flat source utilizes LEDs to tune the counts to be ~constant with wavelength
Note: we never divide data by the flat – it is used only for weighting

## Slide 56: PSF model
Fiber core is well resolved with steep wings due to excellent image quality of spectrographs
  Required to allow clean separation of fibers while still packing the maximum number onto a detector
  Utilize a deterministic image-moment based alignment methodology for the spectrographs
  Achieve contrast significantly better than requirement
VIRUS-P
VIRUS spatial profiles at field center
The PSFs “breathe” with ambient ΔT

## Slide 57: Fiber profiles
Model of profiles is important part of weighting scheme in extraction
  Must accommodate variations within and between channels
Current best choice is sum of:
  A Sersic function for the wings,
  A semi-broad gaussian for the transition,
  A core that is of "generalized gauss-hermite" form, namely a free exponent instead of the gaussian 2 and hermite polynomials from h3-h6.
  Once characterized, only vary centroid, widths and maybe an hermite moment or two, depending on how stable the spectrographs turn out to be
We’re investigating variations between channels and the very broad scattered light component ~4-5% of total
Section of lab data with masked IFU input

## Slide 58: Fiber profiles
Model of profiles is important part of weighting scheme in extraction
  Must accommodate variations within and between channels
Current best choice is sum of
  A Sersic function for the wings,
  A semi-broad gaussian for the transition,
  A core that is of "generalized gauss-hermite" form, namely a free exponent instead of the gaussian 2 and hermite polynomials from h3-h6.
  Once characterized, only vary centroid, widths and maybe an hermite moment or two, depending on how stable the spectrographs turn out to be
We’re investigating variations between channels and the very broad scattered light component ~4-5% of total
Profile of single fiber

## Slide 59: Object identification
Robustness of LAE detection is crucial
  Each frame has an associated error frame which records the error in each pixel
  This error is propagated through all computations
Make use of full information available on the CCD and between the three exposures
  Use 2D image information for source classification and extraction
  We do not know where the objects are in position or wavelength
    But can test for every position and λ
  The three dithered exposures represent 3 observations of the field of view through different masks
    Utilize priors on image quality and transparency from guide probes and wavefront sensors to tie them together

## Slide 60: Quality control
Since practically all resolution elements are viewing sky, the statistics of (flux-mean) within resolution elements are very close to a Χ2 distribution
Significance distribution (σ) deviates ~5% in width from predicted Gaussian
  due to imperfect model of PSF wings and lack of pixel flat for V-P data
  Will be fixed for VIRUS
Statistics provide a robust test of data integrity
  In particular, even small mismatch between the data and the calibration model result in a strong deviation from ideal
VIRUS-P data
Resolution elements

## Slide 61: Cosmic Ray rejection
Simulation of model CRs added to real data
  Having three frames with different spatial masking allows cosmic ray rejection without multiple exposures at each position
  Real objects appear in multiple fibers in each exposure
    with intensities consistent with image quality
    and spectral PSF consistent with spectrograph model
    So even a chance coincidence of CR with the spectrum is easily rejected
Cosmic rays have similar σ (fluxes or significance) but very different Χ2

## Slide 62: Deployment
Sarah Tuttle, Brian Vattiat, Richard Savage, Dave Perry, Darren DePoy, Jennifer Marshall, Jean-Philippe Rheault, Travis Prochaska, Niv Drory, Herman Kriel

## Slide 63: IFU mount and fiber feeds
Dither mechanism with input head mount plate – moves IFUs through precise 260 μm triangular pattern to fill in IFUs
Cutaway of hardware and mechanisms around focus
VIRUS IFUs
HRS or HPF feed
LRS2 IFUs
Input head mount plate
1.5” fiber dia
1.5” dia fibers in 1/3 fill hexagonal close pack

## Slide 64: IFU layout
78 IFUs
16 arcminutes (170 mm)
Input head mount plate by IAG

## Slide 65: VIRUS infrastructure
VSS installed on HET
Enclosures for VIRUS are huge clean rooms with heat removal
Ride on VIRUS support structure (VSS, Good et al Proc SPIE 9145-204 (2014)),
  Lifted by air bearings for azimuth moves; not coupled to the telescope structure except at base
VIRUS Cryogenic System (VCS) supplies LN to each unit to cool detectors
VSS and enclosures
VIRUS enclosure
VIRUS Support Structure

## Slide 66: Replicated Fiber-fed Spectrographs

## Slide 67: Replicated spectrographs in astronomy
Beyond the specific application of VIRUS, the replicated spectrograph concept has an important future
Grasp-spectral power diagram (after Bershady)
  Excellent metric for evaluating survey instruments and IFS
  Lines of constant number of pixels ranging up to 8kx8k
  Assuming f/1.3 camera, 4x15 μm pixels per resolution element and R~1000
Shaded area represents the regime of replicated instruments
  Beyond that mosaics of detectors are needed and instruments become physically challenging
  It is much more cost-effective to slice the field into multiple spectrographs like in VIRUS, MUSE, and LAMOST
Hill, “Replicated Spectrographs in Astronomy,” AOT, Vol 3, Issue 3, 265 (2014)

## Slide 68: Replicated spectrographs on ELTs
ELTs present particular challenges for survey spectrographs
  Growth of instrument and detector size with aperture (at fixed camera f-ratio) becomes extreme
  Pushes the limits of glass availability, mechanical engineering and cost
  Will only partially be mitigated with AO for wide fields
For example, an ELT field with GLAO has 50M spatial elements and thousands of possible targets
  Similar to a 4 m with a three degree field
Efficient use of detector pixels requires image slicing
  Replication offers a cost-effective route
  Deployable fiber IFUs allow image slicing at input and efficient use of pixels in the spectrograph
Hill, “Replicated Spectrographs in Astronomy,” AOT, Vol 3, Issue 3, 265 (2014)

## Slide 69: Summary
VIRUS IFUs contain 700 km of fiber
  Almost exactly the driving distance from Austin to the HET, so we’re at a telecom scale!
The design is simple, and manufacturable on large scale
  Extensive prototyping and testing has led to a durable design
We’re about 60% the way through production and will begin to deploy the IFUs after first light of the upgraded HET, projected for Q2 2015
This is a challenging project for a small team, and the development effort will have spanned 10 years when complete
Lessons learned are very applicable to replicated instruments on the next generation of ELTs

## Slide 70: VIRUS Team and Consortium
University of Texas
Taylor Chonis
Niv Drory
Karl Gebhardt (PS)
John Good
Gary Hill (PI)
Briana Indahl
Herman Kriel (PM)
Martin Landriau
Hanshin Lee
Phillip MacQueen
Emily McLinden
Steve Odewahn
Dave Perry
Trent Peterson
Richard Savage
Matthew Shetrone
Sarah Tuttle (IS)
Brian Vattiat
MPE/USM
Ralf Bender
Maximillian Fabricius
Ulrich Hopp
Francesco Montesano
Jan Snigula
Penn State University
Joanna Bridge
Robin Ciardullo
Henry Gebhardt
Caryl Gronwall
Alex Hagen
Larry Ramsey
Don Schneider
Greg Ziemann
AIP
Svend Bauer
Dionne Haynes
Thomas Jahn
Andreas Kelz
Martin Roth
Matthias Steinmetz
Texas A&M
Richard Allen
Darren DePoy
Ting Li
Jennifer Marshall
Travis Prochaska
Jean-Philippe Rheault
Other Institutions
Josh Adams (OCIW)
Heiko Anwad (IAG)
Guillermo Blanc (OCIW)
Mark Cornell (MIT LL)
Gavin Dalton (Oxford)
Jeremy Murphy (Princeton)
Harald Nicklas (IAG)
Blue=IFU
Notes: 70
Updated with Harald and Dominik Schleicher 6/17