Free Vibrations of a Rigid Cylinder in MIT Towing Tank

Experiment Desciption

Experiments performed by Oyvind Smogeli in 2002.

Documents prepared by Jason Dahl (jdahl@mit.edu), October 2007.

This set of experiments contains data for a rigid cylinder that is allowed to oscillate with free vibrations in the direction transverse to the nominal towing velocity.  The experiments were performed at the MIT Towing Tank in 2002.  The experiments used a force-feedback method for modeling a spring-mass system, by use of the Virtual Cable Testing Apparatus (VCTA).  Fluid forces measured on the cylinder provided feedback for a real time control system that forced the cylinder to move with motions modeled after a free vibration.  A spring-mass-dashpot model was used to describe the structural characteristics of the dynamic system.  The Reynolds number for these experiments was 19,000.  Various damping ratios were tested, with values of one, two, and five, with reduced velocity ranging from 2.6 to 10.  A more detailed description of these experiments, the experimental apparatus, and analysis of the experiments can be found in the following references:

- Smogeli, O. Design and evaluation of a force-feedback control system for VIV

experiments. Thesis, Massachusetts Institute of Technology (MIT) and Norwegian University of Science and Technology (NTNU), 2002.

- Smogeli, O. N., Hover F.S., and Triantafyllou, M.S.  Force-feedback control in

VIV experiments. Proceedings of the International Conference on Offshore Mechanics and Arctic Engineering – OMAE, v 3, 2003, p 685-695.

Data File Description

The posted data files are in the following formats:

.mat		Matlab version 7, saved workspace.  Workspace parameters are explained

below.

The data is given as processed values calculated from time series.  The raw data time series are not given, rather coefficients from the time series, phases, amplitudes, and frequencies are given.

freevib_zeta0_01mod.mat		Free vibration experiment with structural damping

of 0.01.

freevib_zeta0_02mod.mat		Free vibration experiment with structural damping

of 0.02.

freevib_zeta0_05mod.mat		Free vibration experiment with structural damping

of 0.05.

Matlab Workspace Variables

Variable			Description

run				Run number , five digits, first three digits are date, last two

digits are the run number from that day, e.g. 21405 corresponds to Run #5 from February 14.

amp				Amplitude of oscillation in meters

omega				Frequency of oscillation in rad/s

omega_f			Forcing frequency in rad/s

omega_n			Commanded natural frequency in rad/s

mstar				Simulated mass ratio

u				Carriage velocity

dia				Cylinder diameter

clv				Lift coefficient in phase with velocity (mean)

clv_std				Lift coefficient in phase with velocity (standard deviation)

cla				Lift coefficient in phase with acceleration (mean)

cla_std				Lift coefficient in phase with acceleration (standard dev)

clpure				Total hydrodynamic force coefficient (mean)

clpure_std			Total hydrodynamic force coefficient (standard deviation)

phase				Phase between lift and y-motion (mean)

phase_std			Phase between lift and y-motion (standard deviation)

cd				Drag coefficient (mean)

cd_std				Drag coefficient (standard deviation)

ct				Total force coefficient (no inertial correction for cyl mass)

c_incorr			Inertial correction coefficient

zeta				Damping ratio calculated from clv

fy_cross			Cross correlation between lift force sensors (mean)

fy_cross_std			Cross correlation between lift force sensors (std dev)

period				Period of oscillation

rel_amp			amp/dia, non-dimensional amplitude

v_rn				Nominal reduced velocity

v_r				Reduced velocity

rel_freq			omega/omega_n, relative frequency

c_m				Added mass coefficient

omega_a			Actual natural frequency, corrected for c_m