Massachusetts Institute of Technology

Department of Electrical Engineering and Computer Science

6.111 Introductory Digital Systems Laboratory (Spring 2007)

Final Project Check Off Sheet

Project Title: Wireless Headphones

Student Names: Nivedita Chandrasekaran, Jessica Nesvold, Aditi Shrikumar

TA Name: David Wentzloff

TA Signature/Date:

System Level

| Transmit a 3 minute audio file wirelessly to the receiving headphone set. |  |
| --- | --- |
| Compresses the digital signal into a packet form compatible with the wireless transmitter and receiver. |  |
| Transmits and receives packets from distances of at least 20 feet. |  |
| Decompresses the received packets. |  |
| Converts the decompressed digital packets back into analog. |  |
| Outputs the analog signal to headphones. |  |

ADC and DAC (Aditi)

| Finite state machine transition diagrams, block diagrams, and Verilog code. |  |
| --- | --- |
| 5x16bit interface between ADC/DAC and compression/decompression modules. |  |
| Implement serial interface to ADC/DAC. |  |

Compression/Decompression (Jessica)

| Finite State Machine transition diagrams, block diagrams, and Verilog code. |  |
| --- | --- |
| Verilog compression algorithm for use with signed 16-bit integer inputs. |  |
| Verilog decompression algorithm that takes in compressed packets and outputs signed 16-bit integers. |  |
| Working buffer for interfacing to wireless module. |  |

Wireless (Nivedita)

| Finite State Machine transition diagrams, block diagrams, and Verilog code. |  |
| --- | --- |
| Major FSM properly transitions between transmission, reception, and configuration states. |  |
| Wireless chip reset and configured correctly (panID, device ID). |  |
| Transmits packets from FPGA transmit FIFO buffer, resends if necessary. |  |
| Receives packets into FPGA reception FIFO buffer, sends ACK if CRC is correct. |  |
| Transmit a 10 byte packet of data across the lab. |  |