Simulation of a Real Time Factory Control Policy in Multi-Product, Make-to-Order Semiconductor Fabrication Facilities.

by

Todd Andrew Rosenfield

Submitted to the Department of Mechanical Engineering in Partial Fulfillment of the Requirements for the Degree of

Bachelor of Science

at the

Massachusetts Institute of Technology

June 2001

(2001 Todd Andrew Rosenfield

All Rights Reserved

The author hereby grants to MIT permission to reproduce and to distribute publicly paper and electronic copies of this thesis document in whole or in part.

Signature of Author…………………………………………………………………………

Department of Mechanical Engineering

May 17, 2001

Certified by…………………………………………………………………………………

Stanley Gershwin

Senior Research Scientist. Department of Mechanical Engineering

Thesis Supervisor

Accepted by……………………………………………………………………………...…

Ernest G. Cravalho

Chairman, Undergraduate Thesis Committee

Simulation of a Real Time Factory Control Policy in Multi-Product, Make-to-Order Semiconductor Fabrication Facilities.

by

Todd Andrew Rosenfield

Submitted to the Department of mechanical Engineering

on May 17, 2001, in Partial Fulfillment of the

Requirements for the degree of Bachelor of Science in

Mechanical Engineering

ABSTRACT

The performance of the Control Point Policy (CPP) in multi-product, make-to-order semiconductor fabrication facilities with high demand rates is studied.  In particular, the performance of the CPP is studied in situations where particular parts have priority over others.  The CPP is explored in detail through computer simulation experiments.  The results obtained provide insights into the roles of hedging time parameters and consumer lead time in offsetting the poor service levels of low priority parts.

For the cases studied where the service level of one part type is much less than that of the other due to the static buffer priority scheme, attempts were made to use finite hedging times to increase the minimum service level of the system.  Such attempts were mildly successful.  It was found that hedging times as used in the readiness logic can lead to a very small improvement in the minimum service level.  After a good set of hedging times was identified, experiments were conducted to assess the increase in lead times necessary to attain an acceptable service level.  It was determined that an acceptable service level for low priority parts can be obtained with lead times approximately three times the lead time for high priority parts.

Thesis Supervisor: Stanley B. Gershwin

Title: Senior Research Scientist. Department of Mechanical Engineering

# Contents

# 1	Introduction	7

# 1.1	 Background and Objectives………………………………………………………	7

# 1.1.1  Manufacturing Environments……………………………………………...	8

# 1.1.2  Scheduling Policies………………………………………………………...	9

# 1.2	Literature Review………………………………………………………………...	10

# 1.3 Thesis Outline……………………………………………………………………	10

# 2	Production Scheduling Policy and Experiments	11

# 2.1  The Control Point Policy………………………………………………………...	11

# 2.1.1  Terminologies and Definitions……………………………………………	12

# 2.1.2  Scheduling Algorithm…………………………………………….……….	13

# 2.1.3  Policy Implementation…………………………………………………….	14

# 2.2	Performance Measures…………………………………………………………...	14

# 2.3	Simulation Model Description…………………………………………………...	15

# 2.3.1  Simulation Software and Computing Resources………………………….	16

# 2.3.2  Model Assumption and Limitations……………………………………….	16

# 2.3.3  Toy Fab Formulation……………………………………………………...	17

# 2.3.4  Demand Model…………………………………………………………….	19

# 2.4	Statistical Analysis……………………………………………………………….	21

# 3	Solution Technique	22

# 3.1 Intuitive Duscussion……………………………………………………………...	23

# 3.2 Readiness Logic………………………………………………………………….	24

# 3.3 Experimental Procedure………………………………………………………….	25

# 3.3.1  The Control Point Location……………………………………………….	25

# 3.3.2  Formulation of Experimental Cases……………………………………….	26

# 3.3.3 The Hedging Time Parameters…………………………………………….	27

# 3.3.4 The Lead Time Multiple and Hedging Time Paramters…………………...	29

# 3.4	Results……………………………………………………………………………	30

# 3.5 Summary…………………………………………………………………………	33

# 4	Conclusions	35

# 4.1	The CPP Parameters……………………………………………………………...	35

4.2	Recommendations for Further Research…………………………………………	36

# List of Figures

# 2-1	Toy Fab………………………………………………………………………	18

# 3-1	Service Levels for Cases 1 Through 6……………………………………….	31

# 3-2	Part Type Two Service Level Versus Part Type Two Lead Time Multiple For Different Sets of Hedging Times…………………………………………….	32

List of Tables

I	Demand Model Parameters………………………………………………	20

I	Buffer Priority Schemes………………………………………………….	27

II	Performance measures with infinite hedging times……………………...	30

III	Hedging Times for Part Type One Buffers in the Case 5 Priority Scheme

……………………………………………………………………………	32

IV	Part Type One Service Level versus Hedging Time Parameters………...	33

# Chapter 1

Introduction

Manufacturers are strongly motivated to implement a good production scheduling policy.  A good policy the potential for significant cost savings, as well as the ability to meet early due dates consistently.  In fast-paced make-to-order environments such as semiconductor fab, the latter is especially important.

This thesis studies the Control Point Policy (CPP) in multi-product, make-to-order semiconductor facilities (fabs) where one part type has priority over another.  Section 1.1 explains the background and objectives of the study.  Following is a literature review in Section 1.2 and a summary of the thesis in Section 1.3.

  - Background and Objectives

The CPP is a real-time production scheduling policy introduced by Gershwin[1].  Gzouli [2] showed, through extensive simulation experiments, that it performs very well in single part type systems.  In addition, he provides some important insights on the understand of some of its parameters.  In more simulation experiments, Yong [3] shows that in a two part-type-system, service levels are strongly characterized by the CPP’s discrete nature.  The service levels are highly dependent on which buffer is assigned the lowest priority.  Additionally, he develops even more insight into how the various parameters affect the system.  The analysis, however, is not complete.  The CPP is still in the early stages of development and it is not fully understood.  There is no set of guidelines for choosing policy parameters based on the layout of a manufacturing system.  The analysis is carried out through simulation experiments since numerical/analytical methods are not fully developed.

The introduction of multiple part types to the study exponentially increases the number of parameters with each part type and machine.  As such, incredible computing resources would be required to carry out an exhaustive analysis.  This study attempts to characterize the role of some of these parameters through methodical setup and planning of the simulations.

This study is an extension of the first attempt to study the performance of CPP in multiple-part-type systems.  In order to reach a deeper understanding and formulate methods for effective parameter generation, more comprehensive experiments need to be carried out.

1.1.1 Manufacturing Environments

Manufacturing environments have been undergoing many changes due both to changes in manufacturing processes and changes in consumer behavior.

A characteristic of semiconductor fab is re-entrant flow.  Parts re-visit many workstations in the facility several times.  This feature is relatively new and is not present in traditional assembly line manufacturing.  Additionally, workstations no longer consist of a single machine, but of several identical machines working in parallel.  As a result to these changes in the way factories are designed, many new scheduling policies have been developed.

Consumers in today’s market have shifted towards an increasing demand for make-to-order (MTO) products from make-to-stock (MTS).  In a pure MTS system, all parts are interchangeable.  Release of materials into the system is based on the production goal of replenishing the finished goods buffer.  Light bulbs are an example of a product of a MTS system.  On the other hand, in a pure MTO environment, release of materials is independent of what is happening in the facility.  It depends only on the customer orders, which have an associated lead time.  The customer lead time is the amount of time the customer is willing to wait before delivery.  In many cases, the lead time is set by the fab as an estimate of how long the order will actually take.  This environment is implemented for products with very specific customer requirements.  A good scheduling policy is required to meet the due dates consistently.

1.1.2 Scheduling Policies

There are two basic classifications of scheduling policies:  Those that respond to the state of the system and those that do not.  The system state is the result of all the events happening at any given time.  Scheduling policies that make decisions based on this state are called real-time scheduling policies.

Scheduling policies based on demand forecasts and material requirement planning are not real-time, and are not applicable to a MTO environment.  The reason is that manufacturers must be able to determine feasible due dates based on the state of the system for every order.  Using these due dates, the manufacturer can then make scheduling decisions in order to meet as many due dates as possible.

  - Literature Review

Gershwin [1] explains the formulation of the CPP.  He also summarizes the observations on the implementation of the CPP at Boeing.  Gzouli [2] conducts extensive experiments on the CPP in single part systems.  Yong [3] continues Gzouli’s research by applying the CPP to multi-part systems, and studying the effects of various parameters.  Wein [4] offers a classic study of simulation experiments.  He determines that effective control of the release of materials into the system has the greatest effect on reducing mean throughout time.

  - Thesis Outline

Chapter 2 explains the CPP in detail.  It also contains a description of the toy fab, the simulation model used for the simulation experiments in this thesis.  It is a small scale representation of a semiconductor fab.

Chapter 3 begins with the methodological approach to this thesis.  It follows with the results obtained from the simulation experiments.

The thesis wraps up with concluding remarks and suggestions for further research in Chapter 4.

# Chapter 2

Production Scheduling Policy and Experiments

Chapter 1 introduced the characteristics of make-to-stock (MTS) and make-to-order (MTO) environments.  The applicable scheduling policies are different for each environment.

This chapter presents the Control Point Policy (CPP), which can be implemented in an MTO environment.  In combination with the Earliest Due Date Policy, it is used in the simulation experiments performed for this thesis.

Section 2.1 introduces the CPP and the parameters used in its scheduling.  The performance measures used to evaluate the policy are discussed in section 2.2.  The toy fab model that is used for all the experiments of this thesis is described in section 2.3.  Finally, section 2.4 gives a short discussion of the statistical method used to analyze the results of the experiments and ensure their significance.

2.1 The Control Point Policy

The CPP is a real-time scheduling policy introduced by Gershwin [1].  The scheduling decisions are made based on the current state of the system, such as inventory levels, lead time remaining, and machine failure and repair.  This section contains a summary of the CPP scheduling logic, including definitions of terms, the scheduling algorithms, and the requirements for policy implementation.

2.1.1 Terminologies and Definitions

A control point is a resource where the CPP scheduling logic is applied.  Usually, a control point is a machine, but not all machines are control points.  All other resources can be referred to as non-control points.

The policy has three parameters: buffer priority, buffer size, and hedging time.  Each buffer at the control point is assigned a priority ranking.  The scheduling logic uses the priority scheme in the part-selection process.  The term buffer refers to the amount of inventory between consecutive control points.  Because the next control point is likely to be several workstations away, buffer size places a limit on maximum total inventory at all workstations between control points.

The hedging time parameter is used in the readiness condition of the scheduling logic.  Its primary purpose is to impede the flow of materials that are very early compared to their due dates, and thus freeing up resources to handle the delivery of other parts that may be more urgent.  The hedging time is closely related to the remaining cycle time, which is the amount of remaining manufacturing time until the completion of the part.

A part is considered available if it is present at the control point and if the immediate downstream buffer is not full.  It is ready if the sum of the hedging time and the current time is greater than the part’s due date.

A machine at a workstation is considered available if it is operational and idle.  Machines that are in use or undergoing repair or maintenance are not considered available.

2.1.2 Scheduling Algorithm

There are three versions of the CPP scheduling logic:  the time-based, token-based, and surplus-based.  The version presented here is time-based because it is more appropriate for a MTO environment.  For discussion of the other versions, refer to Gershwin [1].

As mentioned in the previous section, the scheduling logic is applied only at the control point.  A simple, sensible policy, such as EDD can be used at other resources.

The real time scheduling logic is listed below.

When a control point becomes available:

- Select the part with the earliest due date from the highest priority buffer.

- Determine if the part is available.  This step is the availability logic.

- If the part is available, determine if it is ready.  This step is the readiness logic.

- When a part from the highest priority buffer is available and ready, load into the available machine.

- Otherwise, repeat the first three steps for the next-highest priority buffer.

- If there are no locally available and ready parts, let the control point remain idle.  This time can be used for other important activities, such as preventative maintenance.

2.1.3 Policy Implementation

Implementation requires setting up the policy in advance and executing it.  The execution is discussed in the previous section.  The following actions are performed in the preparatory phase:

- Select the number of control points and their locations.

- Assign priority to all the buffers in front of each control point.

- Determine hedging times.

- Determine the buffer sizes between control points.

These decisions are made chronologically, even in the preparatory phase.  The hedging times and buffer sizes can only be established after the control points have been chosen.  Additionally, these parameter values will be affected by the buffer priority scheme.

The CPP provides an unambiguous way of selecting which part to load into the machines at any time.  It instructs the operators even when machine failures and other variability disrupt the schedule.  Furthermore, it does not require elaborate calculations.  Good performance may only require scheduling at the control points.  Because not all workstations need to be control points, the implementation cost may be significantly lower compared to other policies.

2.2 Performance Measures

In an MTO environment, it is crucial for the manufacturer to meet the expected delivery date in order to assure customer satisfaction.  This calls for a due date based performance measure.  The service level is defined as the percentage of finished parts that meet their due dates.

In a multi-product system where all the product types are considered equally important, the manufacturer would want to maximize the service level for all customers.  In this case, the minimum service level from all the product types is suitable.  In other cases, the manufacturer may be more interested in maximizing the service level of a particular type of customer that has higher priority than another.  Consequently, a policy that does well in one measure may not do as well in another.  Extent of lateness or earliness is not reflected in the service level.

Frequently there is a tradeoff between service levels and the amount of inventory in the system.  A policy that yields a higher service level will also be required to keep higher levels of inventory.  Consequently, it is prudent to define a performance measure that gauges the amount of work-in-progress inventory (WIP) in the system.  A policy that leads to higher service levels and lower WIP is favored.

Both service levels and WIP are used as performance measures for the simulations performed for this thesis.  The WIP is defined as all the materials in the system, excluding those at raw material buffers.  The reason raw materials are not included in the WIP is that their inventory levels are likely to be influenced by business decisions rather than scheduling rules.

2.3 Simulation Model Description

The CPP is still in the early stages of development, and its behavior is still not fully understood.  As yet, there is no good set of guidelines for choosing policy parameters.  Simulating a real fab with hundreds of workstations and process routes for many different part types does not provide for many choices for the values of each parameter.  Even with a simple two-machine line with 10 buffers, five choices of buffer size for each buffer results in 510 simulation runs, not accounting for repetition to satisfy statistical significance.

Section 2.3.1 describes the simulation software and the computing resources used.  For the analysis of the CPP, a simulation of a simple wafer fab is developed, hereafter referred to as a toy fab.   Section 2.3.2 describes the assumptions made about it and the scheduling policy.  Section 2.3.3 contains a detailed description of the toy fab while the demand model is summarized in section 2.3.4.

2.3.1 Simulation Software and Computing Resources

The simulation software used was originally developed by Gzouli [2] as a multi-platform JAVA based program for single part, one failure mode, and single process flow systems.  It was then modified by Yong [3] to enable the analysis of multiple part types, process flows and machine failure modes.  It has three basic components: one representing the factory, one representing the scheduling policy, and a simulation manager.

The factory module represents the physical state of the system, such as machine failure and repair, and whether each customer’s order due date has been reached.  These states are reported to the simulation manager.  The scheduling policy determines the appropriate response to the events.  The simulation manager relays the decisions back to the factory for implementation.

The program was designed to be able to accommodate different scheduling policies.   For this thesis, only the CPP was studied, but any other scheduling policy could be incorporated into the software.

The computing resources used were Cell2 (Pentium III 700 with 256 MB RAM), Toddroad (Pentium III 450 with 128 MB RAM), and Darkandlight (Dual Pentium III 733 with 768 MB RAM).

2.3.2 Model Assumptions and Limitations

Listed below are the assumptions made for the CPP and the toy fab model.

- The setup time incurred when different part types or different processing steps of the same part type are processed at each workstation is zero.

- Material is transported in units of one, so there are no batches.  Transportation time is zero.

- Machines may operate asynchronously.  Parts can be loaded whenever the scheduling policy permits.

- Machines can fail only while operating

- The raw material supply is assumed to be infinite.  There is no waiting for raw materials.

- The CPP operates under a block-before service (BBS) algorithm.  A part will only be loaded when there is space in the downstream buffer,

- Machine processing times are modeled using lognormal distributions.

- Machine failure and repair times are modeled as exponential variables.

There are several reasons for making these assumptions, the most important of which is that they simplify the analysis by reducing the number of variables to consider.  The BBS assumption serves to standardize the CPP scheduling policy with other scheduling policies, should further research be intended to compare it to other scheduling policies.  The analysis can concentrate on the factory uninfluenced by disruptive effects of upstream supply chains because of the infinite raw material supply assumption.

2.3.3 Toy Fab Formulation

The toy fab, originally designed by Gzouli [2]for a single part type, single process flow was then modified by Yong [3] to incorporate two different process flows for two part types.  It retains many of the characteristics of a semiconductor fab, including re-entrant process flow.  It consists of multi-server workstations made up of several identical machines working in parallel.  In this thesis, the term workstation refers to both single-server and multi-server stations.

Figure 2-1 shows a pictorial representation of the factory model and process flow.   Part type one visits each work station three times each and part type two visits each one twice.

Figure 2-1: Toy Fab

The buffers upstream of each workstation are labeled Bsq, where the subscript s represents the upcoming process step while q denotes the part type.  The raw materials and final goods buffers are labeled as B0q and Bfq respectively.  Each buffer is distinct in its part type and process step.  Due to the re-entrant process flows, there are many more buffers than there are workstations.  The hedging times associated with each buffer are labeled as Hsq, where the subscripts have the same definitions as the buffer subscripts.

Workstation 1 (WS 1), which represents cleaning operations has one machine whose mean processing time is 1 with a very small coefficient of variation (0.02).  Workstation 2 (WS 2), which represents all the operations a part receives before returning to WS 1, has eight identical machines, each with mean processing time of 10 and a coefficient of variance of 0.7, modeling the aggregate variability of all the operations a part goes through downstream of WS 1.  The machine at WS 1 can fail while those at WS 2 do not.  The failure and repair times are included in the processing time variance.

The processing time, which is the same for both parts at every processing step, follows a lognormal distribution.  The total inventory in the system used for the performance measures includes all parts in the fab except the raw material buffers.

The failure, repair, and processing times, and the number of visits to each workstation are chosen such that the line is roughly balanced.  The capacities of both workstations are approximately the same.  Consequently, there are no bottlenecks affecting the selection of the control point.

2.3.4 Demand Model

Many interesting phenomena arise in a MTO environment where customer arrivals and order due dates are uncertain.  Orders that arrive later may have earlier due dates than orders that have already arrived.  The priority of the orders in the system may have to be re-sequenced to accommodate these new orders.  The importance of orders may change over time.  Due to business issues, some part types may become much more important.  Even if different orders are equally important, one particular order may suddenly become very urgent due to customer pressure.

The demand model used by Gzouli [2] and Yong [3] is used in this analysis to model the arrival process as well as the due date, which is defined as the sum of arrival time and the customer lead time, as defined in section 1.1.1.  Because the performance of low demand rate cases did not distinguish among scheduling policies, high demand rate is used in the toy fab.  The average customer lead time is set at 10 times the total in-machine processing time for part type one, but can be much longer for part type two.  Both of these random variables are modeled as normal distributions with coefficients of variation of 0.5 each.

Some important parameters of the demand model are listed in Table I.  The utilizations for each workstation are 94.6% for WS one and 93.3% for WS2.  Wein (1988) describes the computation of utilization.  Utilization is the percentage of time that a workstation is operating on a part.

| Demand Model parameters | Part Type 1 | Part Type 2 |
| --- | --- | --- |
| Average Takt time, t | 6.4 | 7.2 |
| Standard Deviation of order arrival interval, σt | 3.2 | 3.6 |
| Average customer lead time, ℓ | 330 | 220 or higher |
| Standard Deviation of lead time, σℓ | 165 | 110 or higher |

Table I:  Demand Model Parameters

The lead time for part type one is set to a smaller value because part type one is defined to be of higher priority than part type two.  It is in the company’s best interest to ensure a shorter lead time for part type one, although it is more metal layers than part type two.  Additionally, part type one has a higher demand rate in order to represent an increasing demand for more complex parts in the semiconductor industry.

The simulations are run for a total of 300,000 time units with statistics collected over the last 150,000 time units.  This setup is sufficient to ensure that all possible events will occur a large number of times, thereby approximating the steady state behavior of the system

2.4 Statistical Analysis

The simulation output has a random nature.  As such, independent replications of the simulation are needed to obtain statistically significant estimates of the results.  The procedure utilized is to make enough replications until the half-length of the 95% confidence interval divided by the output of interest is less than 3%.

Both service levels and WIP are the outputs of interest.  When the service level of one part type is much higher than that of the other, the relative error of the lower service level may not satisfy the statistical requirement when that of the higher one does.  The guideline used in this thesis is to achieve the relative 3% relative error requirement for the lower service level.  Even though the higher service level part has higher priority, it is important to guarantee a reliable lead time for the customers, even for the low priority part.  On average, we required at least 20 replications of each run.  For good measure, each simulation was replicated 50 times to ensure statistical significance.

# Chapter 3

Solution Technique

The CPP and its scheduling algorithm have been discussed in chapter 2.  One must understand each of the CPP parameters in order to compare it with other scheduling policies.  With more complicated manufacturing systems, many sets of CPP parameters are needed for each part type, workstation, and re-entrant flow.  Their interactions then become more difficult to understand and analyze.

As demonstrated by Yong [3], the buffer priority scheme alone causes clustering of service levels.  When the priority scheme is fixed at either WS 1 or WS 2, the service levels will fall into one of two clusters based on the designation of the lowest buffer priority at the other WS.  The order of the rest of the buffer priorities at that workstation has very little influence on the service levels.  In most of these clusters, the service level of one part type greatly exceeds that of the other.  This is acceptable if one part type has a higher priority than the other.

This phenomenon is not a surprise under the constraint of finite capacity.  Often much more capacity is needed to improve the service level when it is already very close to 100% than when it is much lower.  Thus, a slight decrease in the service level of the more important part type could result in a larger increase in that of the other.

This chapter investigates several things.  It seeks to identify a priority scheme that has the potential for high service levels for both parts.  It intends to identify a set of finite hedging times that can improve the service level of the less important part type over that using infinite hedging times.  Lastly, it uses these hedging times in combination with an increased customer lead time for the less important part type to increase the service levels of both parts to acceptable levels.  These experimental procedures are discussed in Section 3.3.  Preceding these experiments is an intuitive discussion of the CPP in Section 3.1 and a review of the readiness logic in Section 3.2.  Following all these are the results and a summary in Sections 3.4 and 3.5 respectively.

3.1 Intuitive Discussion

In the CPP, part selection begins from the highest priority buffer.  The availability and readiness criteria determine if a part from that buffer should be loaded for the next operation.  If no part from that buffer can be loaded, the scheduler then checks the next highest priority buffer.  This sequence is repeated until either a part is loaded or all buffers are checked.  If no parts are available and ready, then the logic keeps checking until one is.

The multiple-part type transfer flow with re-entrant flow requires the assignment of buffer priority depending on the relative importance of each part type.  The buffer priorities need to be carefully assigned in order to obtain desirable performance measures.  Once the buffer priority scheme is selected, the hedging time and buffer size may be used to help offset the detrimental effects of lowest priority assignment.

3.2 The Readiness Logic

In the CPP scheduling logic, availability and readiness criteria are applied at the control points.  When a part from the highest priority buffer has satisfied both these criteria, then it will be operated on.  Consequently, a full analysis of the scheduling logic must include both criteria.

On the other hand, it will be difficult to understand the role that the readiness logic plays when both it and availability are specified by the scheduling logic.  Furthermore, the complexity of the toy fab does not provide for many choices about appropriate buffer sizes and hedging times that will lead to good performance.  Because of these reasons, the CPP scheduling logic is limited to the readiness condition.

The hedging time parameter is applied only in the readiness condition.  Only when the sum of the hedging time and the current time is greater than the due date will the part be considered ready.  If a buffer hedging time is infinitel, all parts in that buffer are always ready.  Conversely, if a buffer hedging time is very low, then parts will probably have to wait a while before they are processed.  The buffer priority scheme and the performance measure of interest strongly influence what the values of the hedging times should be.

The hedging times and buffer sizes serve only to cause parts to wait longer than they otherwise would.  They can free up resources used by parts that are early enough, but they cannot raise the priority of low priority parts.  The readiness condition has the ability to prevent overflow of materials downstream, reduce overall inventory, and free up resources in case more urgent materials arrive.  Overly conservative control, however, wastes resources and lowers service levels.

3.3 Experimental Procedure

This section details the experimental procedures conducted for this thesis.  It begins with a justification for the choice of control point in Section 3.3.1.  Following that is a discussion on the formulation on the initial cases used in the simulations in Section 3.3.2.   Section 3.3.3 details the determination of a set of hedging times used to attempt to increase the service levels.  Section 3.3.4 combines the use of finite hedging times and large values of lead time for the less important part type in order to achieve acceptable service levels.

3.3.1 The Control Point Location

It is essential to determine how many control points are needed and where to apply them since the readiness criterion is only applied at the control point.  Such decisions are easy to make with only two workstations in the model.

In general, it is desirable to minimize the number of control points in the system.  This in turn minimizes the amount of data that needs to be collected and analyzed as well as the effort required to implement the policy.  Gzouli [2] showed that for a single part type re-entrant system, performance with one control point can be as good as with two.  Gzouli also determined that a control point at the entrance into the toy fab results in higher service levels and lower inventory than with the control point at WS 2.  Despite all this, both workstations are chosen as control points in this simulation.  The reason is that we wish to fine tune the hedging times to maximize system performance, and using two control points gives a higher degree of control than with just one.  In a more complicated simulation with more workstations, one would not want to use all the workstations as control points.

3.3.2 Formulation of Experimental Cases

Because part type one is more important than part type two, the purpose of the first experiment is to identify a set of buffer priorities that yields a high service level for part type one.  The service level of part type two is very low, but experiments later in this chapter will serve to find ways to bring it up without damaging the part 1 service level.

In order to reduce the total number of simulations required, six different priority schemes are used.  Several guidelines are used to determine which ones are chosen.   A priority scheme corresponding to each of the service level clusters identified by Yong is used.  Also, the schemes selected from the different clusters differ only in the selection of the two lowest priority buffers.  The buffer priority schemes used in the experiments are Listed in Table I.

These cases are divided into two groups:  Cases 1, 2, and 3 form the first group and Cases 4, 5, and 6 form the second.  Members within groups differ only in the assignment of the two lowest buffer priorities.

The six cases were simulated using a range of lead time multiples from 10 to 15 for both part types.  The outputs are used to identify the case that has the highest part type one service level.

| Buffer Priority Scheme No. | Workstation (WS) No. | Buffer Priority, in decreasing order of importance |
| --- | --- | --- |
|  |  | 0 | 1 | 2 | 3 | 4 |
| Case 1 | WS 1 | B41 | B22 | B21 | B02 | B01 |
|  | WS 2 | B51 | B32 | B31 | B11 | B12 |
| Case 2 | WS 1 | B41 | B22 | B21 | B02 | B01 |
|  | WS 2 | B51 | B32 | B31 | B12 | B11 |
| Case 3 | WS 1 | B41 | B22 | B21 | B01 | B02 |
|  | WS 2 | B51 | B32 | B31 | B11 | B12 |
| Case 4 | WS 1 | B22 | B41 | B21 | B01 | B02 |
|  | WS 2 | B12 | B11 | B31 | B32 | B51 |
| Case 5 | WS 1 | B22 | B41 | B21 | B01 | B02 |
|  | WS 2 | B12 | B11 | B31 | B51 | B32 |
| Case 6 | WS 1 | B22 | B41 | B21 | B02 | B01 |
|  | WS 2 | B12 | B11 | B31 | B32 | B51 |

Table I:  Buffer Priority Schemes

3.3.3 The Hedging Time Parameter

The buffer priority scheme used is first analyzed using lead time multiple of 10 for both parts, starting with infinite hedging times.  This simulation is chosen to output a service level that is very high for part type one and relatively low for part type two.  It is very imprudent to take a range of random guess at the hedging times.  In the toy fab with 10 buffers in front of a control point, 10 guess of hedging times for each buffer leads to 1010 = 10 billion simulation runs in one replication.

As a result, a set of guidelines for searching for good hedging times are proposed and listed below.  Explanations for each guideline follow.

- The hedging times are only varied for part type one.  Those for part type two are held at infinity.

- The hedging times are varied one buffer at a time, starting with the finished good buffer and working upstream according to the process flow.

- When the downstream hedging times are varied, the upstream values are held at infinity.

- The measures that are used to determine good hedging times are the service levels for both part types.

The hedging times for part 2 remain infinite because hedging times only serve to impede the progress of early parts.  Part 2 will already have a very small service level, and the hedging times for the part type one buffers will be used to impede the early parts of the more important type while freeing up the resources for machining the less important parts.

The reasoning behind the second and third guidelines comes from the intuition that since the flow rate of the WIP upstream has not encountered the downstream processes yet, it hasn’t been affected by the associated readiness logic.  This is not entirely true due to the re-entry within the system and prioritizing of buffers.  By varying a buffer, everything upstream will experience a change in remaining cycle time while everything downstream will not.  The upstream buffers could nullify the downstream buffers by forcing them to wait a long time upstream such that by the time the parts make it through the system, they are late.

The fourth guideline is needed because of the many performance measures in a multi-product system.  It is important to keep part type one service levels as high as possible because it is the most important part type.  It is also important to improve the service level for part type two, but not too much at the expense of part 1.

About eight choices are made for the hedging time of each buffer at each stage in the experiment.  The best performing choice is kept for the proceeding buffer until a hedging time for each part type one buffer is identified.

3.3.4 The Lead Time Multiples and Hedging Time Parameters

A set of hedging times is identified based on the guidelines described above.  Because a goal of these experiments is to specify the parameters that lead to high performance for all service levels, it is necessary to simulate the system using a range of lead time multiples.  The lead time multiple for part type one remains at 10 because of its importance.  The lead time multiple for part type two, however, may be much higher.  The buffer priority scheme dictates that part 1 is more important, and as such, it is acceptable for type two parts to remain in the system much longer.  This section attempts to identify what lead time multiple for part type will lead to acceptable service levels.

Additionally, the experiment calls for more than one set of hedging times, so several sets are used.  Multiplying every hedging time in the scheme identified according to the methods outlined in Section 3.3.3 by the same constant generates a new set of hedging times.  Six additional sets of hedging times are created in this manner.

The hedging times are multiplied by a constant rather than added to a constant because by adding a constant to each hedging time, the flow rates through the system will not change very much.  The differences between consecutive buffers in the process flow will remain the same, so the only buffer that will see significant changes is the first.  By multiplying, the flow rates between the buffers will change, providing different situations to analyze.

3.4 Results

The simulation results are presented in the following tables and figures.  Table II presents the service levels and WIP for all the cases using infinite hedging times and a lead time multiple of 10 for both part types.  Figure 3-1 shows the service levels plotted against each other for the six cases using lead time multiples ranging from 10 to 15.

| Buffer Priority Scheme No. | p1 service level | p1 WIP | p2 service level | p2 WIP | min service level | total WIP |
| --- | --- | --- | --- | --- | --- | --- |
| Case 1 | 0.821 | 39.1 | 0.540 | 37.8 | 0.540 | 76.9 |
| Case 2 | 0.548 | 44.9 | 0.900 | 27.5 | 0.548 | 72.4 |
| Case 3 | 0.938 | 48.7 | 0.338 | 34.1 | 0.338 | 82.8 |
| Case 4 | 0.707 | 58.0 | 0.646 | 19.4 | 0.646 | 77.5 |
| Case 5 | 0.947 | 49.9 | 0.344 | 37.5 | 0.344 | 87.5 |
| Case 6 | 0.560 | 51.4 | 0.946 | 29.4 | 0.583 | 80.8 |

Table II: Performance measures with infinite hedging times

In Figure 3-1, the points closer to the upper right corner of the graph correspond to higher lead time multiples.

Two things can be inferred from these results.  First, Case 5 seems to be the best one on which to focus the rest of the research.  It has the highest part type one service level and a low part type two service level.  Incidentally, it also has a high WIP.  Second, for parts that have a relatively low service level with a lead time multiple of 10, the increase in service level as the lead time multiple increases to 15 isn’t that much.  It seems that in order to obtain high service levels, the lead time multiple for part type two may have to be increased much higher than 15.

Figure 3-1: Service levels for cases 1 through 6

Table III shows the set of hedging times identified according the methods described in Section 3.3.3 as well as the additional sets identified according to the method described in Section 3.3.4.  Figure 3-2 shows the part 2 service levels versus the part type two lead time multiple for all the cases in Table III and case 5 from Table I.

| Case | H01 | H11 | H21 | H31 | H41 | H51 |
| --- | --- | --- | --- | --- | --- | --- |
| 5a | 136 | 124 | 100 | 84 | 64 | 40 |
| 5b* | 170 | 155 | 125 | 105 | 80 | 50 |
| 5c | 204 | 186 | 150 | 126 | 96 | 60 |
| 5d | 238 | 217 | 175 | 147 | 112 | 70 |
| 5e | 272 | 248 | 200 | 168 | 128 | 80 |
| 5f | 306 | 279 | 225 | 189 | 144 | 90 |
| 5g | 340 | 310 | 250 | 210 | 160 | 100 |

*Case 5b is the case identified according to the methods described in Section 3.3.3.

Table III.  Hedging Times for Part Type One Buffers in the Case 5 Priority Scheme

Figure 3-2: Part Type Two Service Level versus Part Type Two lead time multiple for different sets of hedging times.

It is clear from Figure 3-2 that the part 2 service level is not very dependent on the hedging time.  A small increase in performance can be achieved, but nearly all the improvement results from the increase in the lead time multiple.  As noted by Yong [3], the use of finite hedging times does indeed lower the WIP in the system.

Table IV shows the part Type One service level for each of the cases.  It is independent of the part type two lead time multiple, so there is only one relevant data point for each set of hedging times.

| Case | P1 service level |
| --- | --- |
| 5a | 0.762 |
| 5b | 0.848 |
| 5c | 0.892 |
| 5d | 0.914 |
| 5e | 0.927 |
| 5f | 0.934 |
| 5g | 0.940 |
| 5** | 0.947 |

**This datum is included from Table II for ease of comparison.

Table IV:  Part Type One Service Level versus Hedging Time Parameters

The schemes with the higher hedging times result in higher service levels for part type 1.  In fact, nearly the same level of service as with infinite hedging times can be reached while still maintaining a higher part type two service level.

3.5 Summary

This chapter explores the effectiveness of the hedging time parameter as applied to the more important part type under a determined static buffer priority scheme in order to improve the service levels of a two part type system.  In these simulation experiments, the best hedging times are able to slightly increase the minimum service level without offsetting the higher service level very much at all.  In order to raise the minimum service level, the lead time multiple for the poor performing part must be raised to at least 30, which is much higher than for the high priority part type.  The failure of the readiness logic significantly improve system performance is indicative of the limitations of a static priority scheme.

# Chapter 4

Conclusions

This thesis studies the performance of the CPP in multi-product, make-to-order semiconductor fabrication facilities.  Some of its parameters are studied in detail through simulation experiments.  The results obtained provide insights into the roles of some parameters of the CPP in improving system performance when one part is more important than another.

The results are summarized in Section 4.1 with a discussion of the effects of the CPP parameters.  The chapter concludes with a list of possible future research topics in this area.

4.1 The CPP Parameters

The simulations of the six initial test cases use different priority schemes and a range of average customer lead times.  In cases where one part type has a much higher service level due to the priority scheme, the performance of the less important part type is improved only a small amount due to a 50% increase in customer lead time.  A much longer lead time is needed for parts whose service levels suffer due to low priority.

Hedging times were used to attempt to offset the poor performance caused by low buffer priority.  The results show that hedging times can do very little to actually improve the service level, although they do help control the material flows and reduce total work in progress.  The main reason that finite hedging times cannot improve service levels very much is because the readiness logic can do absolutely nothing to control the flow of late parts.

Finally, the results show that the lead time for low priority parts may need to be as high, or ever higher than, 30 times the total cycle time of the part.  Although this is not a desirable figure, it provides for the high priority part to exhibit a very high service level even at a short lead time, 10 times the total cycle.

Further study is required to gain a better understanding of the CPP and its parameters.  Once good guidelines have been established for choosing values for all of the parameters that lead to good performance, the performance of CPP can be gauged on more complicated systems.

4.2 Recommendations for Further Research

The research on the CPP can be extended in several directions.  Some of these include:

- Developing guidelines to select hedging times when minimum service level is used as the performance measure.

- Exploring the performance of the CPP using dynamic buffer priority schemes.

- Comparing the performance of the CPP with other scheduling policies.

# Bibliography

[1]  Gershwin, S. B.  Design and operating of manufacturing systems – the control-point policy.  In IIE Transactions on Design and Manufacturing, Special Issue on Decentralized Control of Manufacturing Systems.

[2]  Gzouli, Omar.  Comparison of scheduling policies by simulation.  Master’s Thesis, Massachusetts Institute of Technology, 2000.

[3]  Yong, Meow Seen.  Simulation of real-time scheduling policies in multi-product, make-to-order semiconductor facilities.  Master’s Thesis, Massachusetts Institute of Technology, 2001.

[4]  Wein, L. M.  Scheduling Semiconductor wafer fabrication.  IEEE Transactions on semiconductor manufacturing, 1(3): 115-130, 1998.